Development of Broadband Access in Europe

Final Results
December 31, 2005 Data

FSS, UL

June 2006

## SLOVENIA

### Population

|  | Inhabitants | % | Density (inhab./km2) |
| --- | --- | --- | --- |
| Total population | 2.003.358 | 100,0% | 100 |
| of which in urban areas | 441.844 | 22,1% | 809 |
| of which in suburban areas | 766.835 | 38,3% | 173 |
| of which in rural areas | 794.679 | 39,7% | 53 |

The Slovenian population is mainly concentrated in suburban (38,3%) and rural (39,7%) areas, with lower average population density.

### General broadband data

|  | 12/02 | 12/03 | 12/04 | 12/05 |
| --- | --- | --- | --- | --- |
| DSL coverage (% of population) | no data available | no data available | no data available | 55% |
| DSL subscribers | 16.735 | 36.960 | 73.730 | 130.602 |
| DSL penetration (% of population) | 0,8% | 1,8% | 3,7% | 6,5% |
| Cable modem subscribers | 8.000 | 28.698 | 38.836 | 63.584 |

| FTTH subscribers | no data available | no data available | 2.503 | 3.848 |
| --- | --- | --- | --- | --- |
| PLC subscribers | no data available | no data available |  |  |
| WLL subscribers | no data available | no data available |  |  |
| Satellite subscribers | no data available | no data available |  |  |
| Total | 24.735 | 65.658 | 115.069 | 198.034 |
| Total penetration (% population) | 1,2% | 3,3% | 5,6% | 9,9% |

In the year 2005 the number of broadband connections to Internet, has grow dramatically, growing almost 50% in the first nine months. The largest proportion of broadband access presents Internet connections that based upon xDSL technology. Operators provide xDSL services either via unbundled local loops or via Telekom Slovenia’s operator broadband access (Telekom Slovenia is wholesale operator of Internet access in Slovenia).

On completion of the analysis 54 cable operators, 5 fixed wireless operators and 17 xDSL operators were registered in the official records of the Post and Electronic Agency of the Republic of Slovenia.

Only Telekom offers wholesale broadband access with a bit rate allowing the provision of xDSL services, while other operators provide broadband access only on the retail level, by leasing infrastructure owned by other entities. There were no providers of fixed wireless broadband access in 2005.

The market development is influenced by:

- In Slovenia the market share of narrowband access is declining in favour of broadband access, most often via xDSL and cable modems, but also via other technologies, like fixed wireless access, Ethernet or others (68% of households and more than 80% of companies that have Internet access, access to it by some kind of broadband connection).

- The dramatic growth of broadband connections can be ascribe to local loop unbundling (what happen in 2005), which allows new market participants to compete by offering data transmission services with high bit rates for always-on internet access for multimedia applications based on xDSL technology and by offering voice telephony services.

- Due to local loop unbundling, a number of new operators enter the market in 2005, what increase competition among operators and also cut down the offer prices.

### DSL coverage and take up

#### Coverage and penetration

The above chart presents DSL coverage in Slovenia, based upon all 193 national municipalities, which were divided upon urban, suburban and rural area based upon survey methodology. Totally 55% of Slovenian population lives in municipalities with DSL coverage.

94% of the urban area population lives in municipalities with DSL coverage. The proportion of DSL among suburban population covers 44% of area, and among rural population only 27% of area.

However, the effective coverage is low because not all PSTN lines are capable to offer DSL, mainly due to distance constraints.

#### Number of DSL accesses by download rate

The chart above presents the national DSL accesses by download rate for 92% of all DSL subscribers, among which 80% of DSL subscribers are in the download rate from 512 kbps to 1 Mbps.

Until 2006 most of the network operators provide mainly DSL services at 1.024 kbps download rate and the upstream at 256 kbps. New xDSL services ADSL2+ have been launched in 2006.

#### Percentage of DSL accesses by type of providers

The chart above presents the national DSL accesses by download rate for 92% of all DSL subscribers, among which 90.5% of DSL lines are directly delivered by incumbent.

### Cable modem access

#### Coverage and penetration

The chart above shows the increase of cable modem subscribers in several years. From 2004 the share of cable modem subscribers increased in 2005 for more than 60%.

### Other broadband access technologies

All other forms of broadband access to Internet (FTTH, PLC, WLL, Satellite), without xDSL and cable modem access present less than 2% of all broadband subscribers.

# Footnotes

The number presented total number of FTTH, PCL, WLL and Satellite subscribers for the end of 2004.

The number presented total number of FTTH, PCL, WLL and Satellite subscribers for the end of 2005.